## Slide 1: Introduction to System Modeling using Simulink

## Slide 2: Simulink介绍
提供图形化界面
调用现有的模块，并把它们连接构成系统的模型
以该模型为对象运行Simulink的仿真程序
观察仿真结果、干预仿真结果
可为各个模块提供参数配置。

## Slide 3: Simulink模块库
输入信号源模块库（sources）；
输出接受模块库（Sinks）;
连续系统模块库（Continuous）;
离散系统模块库（Discrete）;
数学操作模块库（Math Operations）；
…….

## Slide 4: 仿真模型的构成
信号源模块：系统的输入；
被模拟的模块：中心模块，运用Simulink所要解决的问题；
输出显示模块：系统的输出。

## Slide 5: 基本特点
提供了许多如scope(示波器)等的接收模块，用Simulink仿真，具有像做实验一样的图形化显示结果；
具有层次性，通过底层子系统可以构建上层母系统；
对子系统的封装的功能，用户可以自定义子系统的图标和设置参数对话框。

## Slide 6: 建立仿真的基本过程
打开一个空白的Simulink 模型窗口；
在Simulink 模块库浏览界面，将相应模块库所需的模块拖入到编辑窗口；
按照给定的框图修改编辑窗口中模块的参数；
将各个模块按照给定的框图连接起来，搭建所需要的系统模型；
采用菜单或命令窗口输入命令进行仿真分析，观察仿真结果，对不对的地方进行修改；
若结果满意，则完成模型的建立。

## Slide 7: 模块库简介—Commonly Used blocks
将最常用的基本模块集中在一起形成的。

## Slide 8: 模块库简介—Continuous

## Slide 9: 模块库简介—Discontinues

## Slide 10: 模块库简介--Discrete

## Slide 11: 模块库简介—Logic and Bit Operation

## Slide 12: 模块库简介—Lookup Tables

## Slide 13: 模块库简介—Math Operations

## Slide 14: 模块库简介—Sources
信号源模块库包含各种信号生成模块
  模块与子系统输入信号源：In1，Ground, From File, From Workspace
  信号生成器: 其余的

## Slide 15: 模块库简介—Sinks
接收模块库
  模块与子系统输出: Out1
  数据观察器:Terminator, To File, To Workspace
  仿真终止模块:其余的

## Slide 16: Overview of a General Dynamic System
Continuous state dynamics: the first derivative of the state vector is a function of the state, input, and time
Discrete state dynamics: the next value of the state depends on the current state, input and time
Outputs: the output value is a function of states, inputs and time.

## Slide 17: Electronic Throttle Control (电子油门控制系统)

## Slide 19: Layout

## Slide 20: Modeling Sensor
Define the potentiometer(电位计) system
Simulate the model and analyze results

## Slide 21: Defining the System and Identifying Its Components
One of the outputs of the throttle subsystem is its angle. This is computed in radians and needs to be translated to degrees for analysis, and then translated to voltage for use in the controller by a potentiometer.
Before modeling the system with equations, answer the following questions:
  How many inputs?
  How many outputs?
  How many states?
  What are the parameters?
  Are there any intermediate signals?

## Slide 22: Modeling the System with Equations
the relationship between the angle in radians, u, and the position in volts, y.
Computing y using a lookup table angles between 0o and 90o.

## Slide 23: Starting Simulink

## Slide 24: Using the Simulink Library Browser

## Slide 25: Building a Block Diagram for the Model

## Slide 26: Adding Blocks
To add blocks, drag and drop them from the Simulink Library Browser into the model.

## Slide 27: blocks
(Sources)输入信号的接口： In1
(Sink)输出信号的接口：Out1
(Math Operation)增益模块Gain,设置信号放大的倍数；
(Lookup Table)基本一维表格查询模块
  低版本：Lookup Table;
  高版本2011a: 1-D Lookup Table

## Slide 28: Connecting Blocks
To connect blocks, select the output port of the source block, and then left-click and drag a line to the destination block.

## Slide 29: Defining the Block Parameters
To view and modify block parameters, double-click the block icon.

## Slide 30: Defining the Lookup Table Parameters

## Slide 31: Defining the parameter Values Using MATLAB®

## Slide 32: Labeling Blocks and Signals
To rename a block, click the block label and edit.
Block labels must be unique.
To label a signal, double-click the signal line and enter text.

## Slide 33: Defining the System Output
Signals can be loaded from the MATLAB workspace.
  Simulation Configuration Parameters Data Import/Export
  Define t and u in the MATLAB workspace
    >>t= linspace(1,10,101)’;
    >>u=linspace(0,pi/2,101)’;

## Slide 34: Defining the System Output

## Slide 35: Simulating the Model and visualizing the Response
Visualize the simulations response:
  >>plot(t,u,tout,yout,’k:’)
  >>xlabel(‘simulation time’)
  >>legend(‘input angle (rad)’ , ’output (volts)’)

## Slide 36: Adding Signal Viewers

## Slide 37: Modifying the Viewer Parameters

## Slide 38: Controlling the Vertical Limits of the Viewer
Open the axis properties dialog box by selecting Axes properties from the context menu after right-clicking →preperty in the axis.

## Slide 39: Data from file

## Slide 40: Overview of Simulink® Solver
Model is simulated using a series of discrete time steps.

## Slide 41: Modeling PWM conversion system
Model comparisons and decision statements
Model the PWM conversion system
Vector signals
Embedded MATLAB® Function block.

## Slide 42: Approaches to Modeling Programming Constructs
Common programming constructs
  Relational comparisons(<, >, ==, etc.)
  Logical operators( AND, OR, NOT, etc.)
  Decision statements(if-else, switch-case, etc.)
  Loop constructs(for-loop, while-loop, etc.)

## Slide 43: Modeling Comparisons
blocks are in the Logic and Bit Operation library

## Slide 44: Modeling Decision Statements
blocks are in the Signal Routing library
Switch模块的第二个信号与阈值的比较，若真，执行上面的赋值为3，否则赋值为-3；

## Slide 45: Modeling Decision Statements
blocks are in the Signal Routing library
Multiport Switch模块的第一个信号与阈值的比较，若为1，执行第二行的赋值，若为2,3，依次为执行第三、四的赋值；

## Slide 46: Extracting and Combining Data Using Vectors
Most blocks are in the Signal Routing library
  Mux-----Concatenate two or more signals into a vector signal
  Demux-----Split a vector signal into separate signals
  Selector-----Output specific elements of a vector signal，（用于从向量中、矩阵或多维信号中选择输入元素）。

## Slide 47: Defining the System and Identifying Its Components
The variables in this system are the controller output(u), duty, and direction
  The controller output, u, is the system input.
  Duty and direction are the system outputs.
  There are no state or parameters to this system both duty and direction are computed directly from the input signal.

## Slide 48: Modeling the System with Equations
The system input is u. duty and direction are the system outputs.
The duty is constrained to fall within the range of 0<=duty<=1.

## Slide 49: blocks
Abs: 求一个数的绝对值；
Saturation：饱和度模块，对一个信号限定上下限，当输入在有Lower limit 和Upper limit参数指定的范围内时，输入信号无变化输出。若超出，则信号就被限幅（值为上限或下限）

## Slide 50: Building a Block Diagram for the Model

## Slide 51: Zero Crossing Detection
Blocks with discontinuous behavior can cause the solver to take additional time steps before and after a discontinuity.

## Slide 52: Modeling Logic with Embedded MATLAB® Function Blocks
using Embedded MATLAB Function block in user defined function library

## Slide 53: Understanding the Embedded MATLAB® Function Block
Embedded MATLAB Library
  Supported functions are simulated via code generation
  Non-supported functions call MATLAB interpreter

## Slide 54: PI controller system modeling
Define the PI controller system
Define discrete states
Create a model of the PI controller
Model discrete transfer functions and state-space systems

## Slide 55: Defining the System
The proportional integral (PI) controller is the throttle plate position controller.
It receives throttle position sensory information and throttle position command information,
and then determines the needed motor-control voltage, the corresponding pulse-width modulation duty cycle, and direction to produce the needed voltage.

## Slide 56: Defining Discrete System Characteristics
Dynamics are updated at a finite time interval referred to as the sample time.
System outputs can depend on memory elements (referred to as discrete states), system inputs, and/or time.
The mathematical representation of a discrete-state system is:
  State update equation:
x(k)=f(x(k-1),u(k),k)
  Output equation:
y(k)=f(x(k),x(k-1),…, u(k),k)

## Slide 57: Modeling Difference Equations
The Unit Delay block in Discrete block set is the generic building block of difference equations.
  It holds and delays its input for a sample period.
  It requires a sample time and initial conditions.

## Slide 58: Modeling Difference Equations (Continued)
Determine the number of Unit Delay blocks required (one for each sample difference):
  For example, x(k)=x(k-1)+u(k)-u(k-1)
  Two are necessary: x(k)=>x(k-1), u(k)=>u(k-1)
Starting with the Unit Delay blocks, provide proper labels to their input and output signals.
Construct its right side one difference equation at a time.
Connect the returned signal of its right side as a source to its left side if necessary.
Set the sample time and assign initial conditions.

## Slide 59: Modeling the System with Equations
A discrete PI controller is used as the throttle position controller based on the following equation.
y(k)=yp(k)+yi (k)
where
yp(k)=Kpe(k)
yi(k)=yi(k-1)+KiTse(k)
-1<yi(k)<1
e(k)——Error(difference between desired output and actual output)
Ts —— Sample Time
Kp—— Proportional gain
Ki—— Integral gain

## Slide 60: Building a Block Diagram Model of the System
y(k)=yp(k)+yi (k)
yp(k)=Kpe(k)
yi(k)=yi(k-1)+KiTse(k)
-1<yi(k)<1

## Slide 61: Modeling Throttle system
Define the throttle system
Create a model of the throttle system
Define continuous states
Simulate the model and analyze results
Model impact dynamics

## Slide 62: Defining the System
The electronic throttle body opens and closes the throttle plate valve in accordance with the accelerator pedal effort, and controls the amount of an inducted into the engine.

## Slide 63: Defining Continuous-State System Characteristics
Dynamics are updated at an infinitesimal time interval.
System outputs depend on memory elements referred to as continuous states, system inputs, and/or time.
Rates of continuous states govern the variation of system dynamics.
The mathematical representation of a continuous-state system is

## Slide 64: Difference equation(差分方程)
Definition
  微分方程的离散化，一个微分方程不一定可以解出精确地解，但把它变成差分方程，离散化后，就可以求出近似的解。
dy+y*dx=0 ,y(0)=1 是一个微分方程的， x取值[0,1] (注： 解为y(x)=e^(-x));
要实现微分方程的离散化，可以把x的区间分割为许多小区间 [0,1/n],[1/n,2/n],...[(n-1)/n,1]

## Slide 65: Difference equation(差分方程)
微分方程可以离散化为差分方程：
y((k+1)/n)-y(k/n)+y(k/n)*(1/n)=0， k＝0,1,2,...,n-1 （n 个离散方程组）
利用y(0)=1的条件，以及上面的差分方程，就可以计算出 y(k/n) 的近似值了。

## Slide 66: Modeling Differential Equations
Solve the equation for the highest order derivative term.
Determine the number of Integrator blocks required (one for each order of derivative) which blocks are in the continuous library.
Starting with the Integrator blocks, provide proper labels to their input and output signals.
One ordinary differential equation at a time, construct its right-hand side.
Connect returned signal of its right side as a source to its left side if necessary
Assign initial conditions.

## Slide 67: Identifying the System Components
System Input:
T(t) = Torque

## Slide 68: Modeling the System with Equations

## Slide 69: Continuous blocks
Integrator:只有初始条件
Integrator Limited: 上下界是有限制的。

## Slide 70: Building a Block Diagram form the Model

## Slide 71: Defining Block Parameters
初始条件：
参 数：

## Slide 72: Defining the System I/O
  Simulation Configuration Parameters Data Import/Export

## Slide 73: Modeling Physical Boundaries (Integrator, Second-Order)
Angular velocity is zero when angle is saturated.

## Slide 74: Introducing Subsystems
Using subsystems has these advantages:
  It helps reduce the number of blocks displayed in you model window
  It allows you to keep functionality related blocks together
  It enables you to establish a hierarchical block diagram

## Slide 75: Creating subsystems
Add a subsystem block to your model, open that block, and add the blocks to the subsystem window
Select the blocks that make up the subsystem, and then select Edit→Creat subsystem
Example

## Slide 77: Handling cross-system gateways
After creating a subsystem, notice that inports and outports are automatically inserted and connected.
Inport and outport are the gateways between the subsystem and its parent
Each inport/outport is associated with an input/output port of the subsystem
The block label is the same as the port name

## Slide 78: Using subsystems to create a visual hierarchy
Subsystem can been dragged and dropped into other models.
Ways
  Open two models
  Copy the subsystem into the other model
  Simplify the diagram by making a subsystem
example

## Slide 80: Summary
Build a continuous system
Build a discrete system
Build subsystem