## Slide 1
汇报人：张建夫 郑凯夫 孙涵彬
时间：2025/11/28
求实创造 为人师表
author：Kai Lei , Guanjie Lin , Meimei Zhang, Keke Li, Qi Li, Xiaojun Jing, and Peng Wang
Measuring the Consistency
Between Data and Control Plane in SDN

## Slide 2
JUNE 12th
求实创造 为人师表
A Brief Introduction to SDN
00
应用层面
控制层面
数据层面
Inconsistency
（不一致性）
SDN:software defined network(软件定义网络)

## Slide 3
1
3
security risks ：bypass firewalls
performance degradation ：cause forwarding loops
packet loss ：lead to black holes
2
Why is Inconsistency a Problem
00

## Slide 4
OpenFlow switches don't confirm
every single rule installation.
01.Lack of Acknowledgement
Software bugs or hardware faults may
cause a switch to ignore priority levels.
02.Switch Failures
Attackers or 3rd-party tools (like ONIE) might
tamper with rules directly.
03.External Modifications
Asynchronous updates lead to
transient inconsistencies.
04.Network Updates
Main Causes for this Inconsistency
00

## Slide 5
Out-of-band (using probe packets)
Existing Solutions and their limitations
00
（使用探测包）
（在真实流量中使用标签）
Pros: No tag overhead.
Cons: Too Slow. Minutes to generate probes (Unsuitable for dynamic networks).
Pros: Real-time checks.
Cons: High Storage Overhead
(Stores path hop-by-hop).
In-band (using tags in real traffic)
2MVeri Approach
2MVeri aims to be In-band, low overhead, and capable of precise fault localization.
Many cannot pinpoint which switch failed.

## Slide 6
1
Packet Processing
Carried out on switches to update tags.
3
Localization
Triggered only when verification fails.
2
Verification
Carried out on the controller to check consistency.
Three Subsystems
of 2MVeri

## Slide 7
A 16-bit Bloom Filter (BF)
Records switch IDs.
A 2D Vector ((v1,v2))
Captures path state.
A Modulus (p)
Prevents overflow.
Packet Processing
01
求实创造 为人师表
Each switch holds a unique 2x2 Characteristic Matrix assigned by the controller.

## Slide 8
Initialization
At the Entry Switch, we sample a flow. We initialize the vector
(v1,v2) and the modulus p.
Reporting
At the Exit Switch, the tag is stripped and sent to the controller.
Update
This is the critical part. At each Internal Switch Si, the tag is updated using this formula:
vnew=(vold×Mi)%p.
Packet Processing
01

## Slide 9
Bloom Filter
Vector Update
Modulus Update
The switch multiplies the current modulus p by its own matrix determinant. pnew=p*det(M). This causes the modulus to grow hop-by-hop.
The vector is multiplied by the switch Matrix M, and then modulo is applied using the newly updated modulus.
The switch ORs its ID into the filter to record its presence.
Packet Processing
04

## Slide 10
Verification
01
求实创造 为人师表
Controller:
Contains global topology & path expectations.
Process:
1.Look up Expected Path for Flow F
2.Compute Tagcorrect using matrices of expected switches.
3.Receive Tagreported from Exit Switch.
4.Compare: if (Tag_rep == Tag_corr) return Consistent;

## Slide 11
Localization
03
求实创造 为人师表
Visual
A tree structure rooted at the Exit Switch.
Core Idea
Use Inverse Matrix (M−1) to "undo" the multiplication
Stop Condition
Path Length == TTL Difference.
Goal
Find path back to Entry Switch.

## Slide 12
Localization
03
求实创造 为人师表
Check2:The Integer Property
This is the mathematical guarantee.
We calculate V×M−1.
Check1:The Bloom Filter
Is the neighbor's ID present in the reported Bloom Filter? This is a fast filter.

## Slide 13
Theoretical Rationale
PART-04

## Slide 14
Modulus
00
Now, we must address a theoretical challenge. How to choose Modulus?
Lemma 1
Problem 1
We solved this with Lemma 1.
The Idea: we set the Modulus p to be a multiple of the determinants of the matrices along the path.
The Proof: We proved that Dnew = Dold ∗A−1 will always result in integers if the modulus encompasses the determinant.

## Slide 15
2.Determinants should be small integers (like 3 or 4) to keep the modulus from growing too fast, yet strictly >2 to avoid high false negatives.
1.Column vectors cannot be multiples of each other (to ensure invertibility).
Other Rationale
01

## Slide 16
Evaluation
PART-05

## Slide 17
Experiment Setup
00
1、Fat Tree topologies （k=4 and k=6）
2、Stanford Backbone
Representing standard data center architectures.
A real-world wide area network topology to ensure our solution works in complex, non-regular environments.

## Slide 18
Scenario 1: Black Hole.
We modified a switch rule to drop packets. 2MVeri detected the missing tags immediately.
Scenario 2: Path Deviation.
We forced a switch to forward packets to a wrong port. The verification failed because the matrix multiplication result didn't match the expected value. 2MVeri successfully recovered the actual path and located the deviating switch.
Scenario 3: Forwarding Loop.
We created a loop between two switches. The reported tag became inconsistent due to repeated multiplications.
Function Test
03
求实创造 为人师表

## Slide 19
Verification Accuracy & Localization Accuracy
01
With a determinant ≥3 , 2MVeri achieves 100% Verification Accuracy and 99.8% Localization Accuracy. This empirically proves our theoretical choice of using cumulative determinants (行列式累乘）.
Now, let's look at the quantitative data. This is crucial. We analyzed how the Matrix Determinant affects accuracy.

## Slide 20
Overhead
01
Storage Overhead
Computation Overhead

## Slide 21
Futrue Work & Recap
PART-06

## Slide 22
First, Protocol Independence
Currently, our implementation is tailored for the IPv4 scenario. We plan to extend 2MVeri to scenarios where multiple protocols coexist.
Second, P4 Implementation
We are looking to migrate the framework from Open vSwitch to P4 programmable switches. P4 offers greater flexibility and programmability, which would allow 2MVeri to run entirely in the data plane hardware, further reducing latency.
Third, Edge Cases
Our paper notes a specific challenge: what if the actual path is the same as the expected path, but the rules matched on the switches are different? We plan to conduct further research to detect this subtle form of inconsistency.
Futrue Work
03
求实创造 为人师表

## Slide 23
Innovative Design
It is the first framework to exploit Matrix Multiplication combined with Modular Arithmetic for in-band path verification. This theoretically solves the overflow problem while preserving path information.
High Accuracy
Through rigorous math proofs and experiments, we achieved 100% verification accuracy and 99.8% fault localization accuracy, outperforming existing solutions.
Low Overhead
By reusing existing header fields and requiring only constant control plane storage, 2MVeri is highly efficient and scalable for large networks.
Advantages Recap
03
求实创造 为人师表