## Slide 1
Computer Networks
第四章习题讲解
王廷
华东师范大学 软件工程学院 Email: twang@sei.ecnu.edu.cn
Office: 理科大楼B1116室

## Slide 2
第四章习题讲解
1. A group of N stations share a 56-kbps pure ALOHA channel. Each station outputs a 1000-bit frame on average once every 100 sec, even if the previous one has not yet been sent (e.g., the stations can buffer outgoing frames). What is the maximum value of N?。
Ans: With pure ALOHA, the usable bandwidth is 0.184 × 56 kbps = 10.3 kbps. Each station requires 1000bits/100s=10 bps, so N = 10300/10 = 1030 stations.

## Slide 3
第四章习题讲解
2. How long does a station, s, have to wait in the worst case before it can start transmitting its frame over a LAN that uses the basic bit-map protocol?
Ans: The worst case is where all stations want to send and s is the lowest-numbered station. Wait time N bit contention period + (N − 1) × d bit for transmission of frames. The total is N + (N − 1)d bit times.

## Slide 4
第四章习题讲解
3. Consider building a CSMA/CD network running at 1 Gbps over a 1-km cable with no repeaters. The signal speed in the cable is 200,000 km/sec. What is the minimum frame size?
Ans: Propagation delay is 1/200000=5 μsec. So, the minimum frame transmission time is 2*5 μsec =10 μsec. This means, in the worst case, a station needs to transmit for a period of 10 μs to detect the collision.
The minimum size of the frame is 1000 Mbps × 10 μs = 10000 bits or 1250 bytes.
Transmission delay >= 2 * Propagation delay

## Slide 5
第四章习题讲解
4. An IP packet to be transmitted by Ethernet is 60 bytes long, including all its headers. If LLC is not in use, is padding needed in the Ethernet frame, and if so, how many bytes?
Ans: The minimum Ethernet frame is 64 bytes, including both addresses in the Ethernet frame header, the type/length ﬁeld, and the checksum. Since the header ﬁelds occupy 18 bytes and the packet is 60 bytes, the total frame size is 78 bytes, which exceeds the 64-byte minimum. Therefore, no padding is used.

## Slide 6
第四章习题讲解
5. Store-and-forward switches have an advantage over cut-through switches with respect to damaged frames. Explain what it is.
Ans: Store-and-forward switches store entire frames before forwarding them. After a frame comes in, the checksum can be veriﬁed. If the frame is damaged, it is discarded immediately. With cut-through, damaged frames cannot be discarded by the switch because by the time the error is detected, the frame is already gone. Trying to deal with the problem is like locking the barn door after the horse has escaped.

## Slide 7
End
Chapter 4