## Slide 1: COMPUTER NETWORKS
Chapter 3 The Data Link Layer

## Slide 2
Responsible for delivering frames of information over a single link
Handles transmission errors and regulates the flow of data

## Slide 3: Nodes and Links
A data unit from one point in the Internet needs to pass through many networks (LANs and WANs) to reach another point. Theses LANs and WANs are connected by routers.
It is customary to refer to the two end hosts and the routers as nodes and the networks in between as links.

## Slide 4: Two Categories of Links
A point-to-point link uses the whole capacity of the medium.
  dedicated to the two devices
  E.g., when two friends use the traditional home phones to chat, they are using a point-to-point link;
A broadcast link uses only part of the capacity of the link.
  shared between several pairs of devices.
  E.g., when the same two friends use their cellular phones, they are using a broadcast link (the air is shared among many cell phone users).

## Slide 5: Two Sublayers of the Data Link Layer
Data Link Control (DLC) sublayer deals with all issues common to both point-to-point and broadcast links.
Media Access Control (MAC) sublayer deals only with issues specific to broadcast links.

## Slide 6: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 7: Data Link Layer Design Issues (1 of 2)
Network layer services
Framing
Error control
Flow control

## Slide 8: Data Link Layer Design Issues (2 of 2)
Relationship between packets and frames
Link layer accepts packets from the network layer, and encapsulates them into frames that it sends using the physical layer;
reception is the opposite process
Reason for encapsulation and decapsulation:
- the link-layer addresses are normally different
- each link may be using a different protocol with a different frame format.
Notes: Assume a person needs to travel from her home to her friend’s home in another city.
The traveller can use three transportation tools. She can take a taxi to go to the train station in her own city, then travel on the train from her own city to the city where her friend lives, and finally reach her friend’s home using another taxi. Here we have a source node, a destination node, and two intermediate nodes.
The traveller needs to get into the taxi at the source node, get out of the taxi and get into the train at the first intermediate node (train station in the city where she lives), get out of the train and get into another taxi at the second intermediate node (train station in the city where her friend lives), and finally get out of the taxi when she arrives at her destination.
A kind of encapsulation occurs at the source node, encapsulation and decapsulation occur at the intermediate nodes, and decapsulation occurs at the destination node.
Our traveller is the same, but she uses three transporting tools to reach the destination.

## Slide 9: Services Provided to The Network Layer (1 of 2)
(a) Virtual communication. (b) Actual communication.

## Slide 10: Services Provided to The Network Layer (2 of 2)
Actual services vary from protocol to protocol
Three possible services
  Unacknowledged connectionless service
    Frame is sent with no connection / error recovery
    Ethernet is example
  Acknowledged connectionless service
    Frame is sent with retransmissions if needed
    Example is 802.11
  Acknowledged connection-oriented service
    Connection is set up; rare

## Slide 11: Framing
Framing methods
  Byte count
  Flag bytes with byte stuffing
  Flag bits with bit stuffing
  Physical layer coding violations
    Use non-data symbol to indicate frame
Framing: breaking up the bit stream into frames

## Slide 12: Framing: Byte count
A byte stream. (a) Without errors. (b) With one error.
Frame begins with a count of the number of bytes in it
    Simple, but difficult to resynchronize after an error

## Slide 13: Framing: Flag bytes with byte stuffing
(a) A frame delimited by flag bytes. (b) Four examples of byte sequences before and after byte stuffing.
Special flag bytes delimit frames; occurrences of flags in the data must be stuffed (escaped)
  Longer, but easy to resynchronize after error
  依赖于8位字符
Need to escape extra ESCAPE bytes too!

## Slide 14: Framing: Flag bytes with bit stuffing
Bit stuffing. (a) The original data. (b) The data as they appear on the line. (c) The data as they are stored in the receiver’s memory after destuffing.
Stuffing done at the bit level
  Frame flag（01111110） has six consecutive 1s (not shown)
  On transmit, after five 1s in the data, a 0 is added
  On receive, a 0 after five 1s is deleted

## Slide 15: Framing – Physical layer coding violations
物理层编码违例法，以曼彻斯特编码为例：
  数据比特‘1’编码成“高-低”电平对，数据比特‘0’编码成“低-高”电平对。
  “高-高”电平对和“低-低”电平对是违例编码。可以利用这些违规编码来定界帧的起始和终止。

## Slide 16: Error Control
Ensuring all frames are eventually delivered:
  To the network layer at the destination
  In the proper order
Ensures reliable, connection-oriented service
Requires acknowledgement frames and timers
Error detection
Acknowledgement
Retransmission

## Slide 17: Flow Control
Controlling the sending of transmission frames at a faster pace than they can be accepted
Feedback-based flow control
  Receiver sends back information to the sender giving it permission to send more data
  Or receiver tells the sender how the receiver is doing
Rate-based flow control
  Protocol has a built-in mechanism
  Mechanism limits the rate at which senders may transmit data
  No feedback from the receiver is necessary
Flow control is a topic in the Link and Transport layers.
Notes:   Rare in the Link layer as NICs run at “wire speed”
    Receiver can take data as fast as it can be sent

## Slide 18: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 19: Type of Errors
Single-bit error means that only 1 bit of a given data unit (such as a byte, character, or packet) is changed from 1 to 0 or from 0 to 1.
Burst error means that 2 or more bits in the data unit have changed from 1 to 0 or from 0 to 1.

## Slide 20: Error Detection and Correction
Error codes add structured redundancy to data so errors can be either detected, or corrected.
The correction of errors is more difficult than the detection.
In error detection, we are only looking to see if any error has occurred. The answer is a simple yes or no. We are not even interested in the number of corrupted bits. A single-bit error is the same for us as a burst error.
In error correction, we need to know the exact number of bits that are corrupted and, more importantly, their location in the message.

## Slide 21: Error Bounds -- Hamming distance
Code turns data of m bits into codewords of n bits
  n = m + r, m data bits and r redundant check bits.
Hamming distance is the minimum bit flips to turn one valid codeword into any other valid one.
Hamming distance of a code is the minimum distance between any pair of valid codewords.
  Example with 4 codewords of 10 bits (m=2, r=8): 0000000000, 0000011111, 1111100000, and 1111111111
  Hamming distance is 5
Bounds for a code with a minimum hamming distance :
  – can correct errors
  – can detect errors

## Slide 22: Explanation of Error Bounds
Errors are detected by receiving invalid codewords.
  从一个正确的码字出发任意走d步（也就是最多有d位出错）都不会到达另外一个正确的码字，但是走d+1步就有可能到达另外一个正确码字，也就是说错了d+1个位以后被当成无错的码字接受。
Errors are corrected by mapping a received invalid codeword to the nearest valid codeword, i.e., the one that can be reached with the fewest bit flips.
  从一个正确的码字出发任意走d步都还是离这个码最近，离另外一个正确的码字至少有d+1步距离，因此纠错时只要知道错误不超过d位就能够将其对应纠正到最近的正确码字。
Notes: If there are more than d bit flips, then the received codeword may be closer to another valid codeword than the codeword that was sent. For example, sending 0000000000 with 2 flips might give 1100000000 which is closest to 0000000000, correcting the error. But with 3 flips 1110000000 might be received, which is closest to 1111100000, which is still an error.

## Slide 23
HDistance=2
HDistance=3

## Slide 24: Exercises
Find the minimum Hamming distance of the following coding scheme:
00000, 01011, 10101, 11110
dmin in this case is 3
This code can detect up to two errors,
and it can correct up to one error.

## Slide 25: Linear Block Codes
Almost all block codes used today belong to a subset called linear block codes.
A linear block code is a code in which the result of XORing any codeword with any other codeword is a valid codeword.
E.g., the code schemes on the previous slides
00000, 01011, 10101, 11110
00000
01011
-----
01011
01011
10101
-----
01011
10101
11110
-----
01011
00000
11110
-----
11110
00000
10101
-----
10101
01011
11110
-----
10101

## Slide 26: Error Detection and Correction
Error-correcting codes
  Referred to as FEC (Forward Error Correction)
  Include enough redundant information to enable the receiver to deduce what the transmitted data must have been
Error-detecting codes
  Include only enough redundancy to allow the receiver to deduce that an error has occurred (but not which error) and have it request a retransmission
Key consideration is the type of errors likely to occur

## Slide 27: Error-Correcting Codes
Hamming codes
Binary convolutional codes
Reed-Solomon codes
Low-Density Parity Check codes

## Slide 28: Hamming Codes
Hamming codes provide for FEC using a “Block Parity”
Allows correction of single bit errors
This is accomplished by using more than one parity bit
Each computed on different combination of bits in the data
Positions of Redundancy Bits

## Slide 29: Single Error Correction
To design a n-bit code with m message bits and r check bits that will allow all single errors to be corrected, we must have
Each of legal messages has n illegal codewords at a distance of 1 from it, formed by systematically inverting each of n bits in a n-bit codeword formed from it.
legal messages requires n+1 bit patterns dedicated to it. The total number of bit pattern is

## Slide 30: Data and redundancy bits of Hamming Codes
Number of data bits m | Number of redundancy bits r | Total bits m + r
1 | 2 | 3
2 | 3 | 5
3 | 3 | 6
4 | 3 | 7
5 | 4 | 9
6 | 4 | 10
7 | 4 | 11

## Slide 31: Redundancy Bits Calculation
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1
2
3
4
5
6
7
8
9
10
11
r8r4r2r1

## Slide 32: Example

## Slide 33: Error Correction using Hamming Code

## Slide 34: Burst error correction using Hamming code

## Slide 35: Summary of Hamming code
Example of an (11, 7) Hamming code correcting a single-bit error
Hamming code gives a simple way to add check bits and correct up to a single bit error:
  Check bits are parity over subsets of the codeword
  Recomputing the parity sums (syndrome) gives the position of the error to flip, or 0 if there is no error

## Slide 36: Convolutional codes
The NASA binary convolutional code used in 802.11
Operates on a stream of bits, keeping internal state
  Output stream is a function of all preceding input bits
  Bits are decoded with the Viterbi algorithm
  Widely used in GSM mobile phone system, satellite communications
Since 1 input bit produces 2 output bits, the code rate is 1/2.
It takes seven shifts to flush an input completely so that it does not affect the output. The constraint length of this code is thus k = 7.
… 1 1 1
0 1 1
1 0 1
…

## Slide 37: Reed-Solomon and Low-Density Parity Check codes
Reed-Solomon codes
  Linear block codes. Often systematic
  Codes are based on the fact that every n degree polynomial is uniquely determined by n + 1 points
  DSL, data over cable, satellite communications, CDs, DVDs, and Blu-ray discs
LDPC (Low-Density Parity Check) codes
  Linear block codes
  Each output bit is formed from only a fraction of the input bits
  Practical for large block sizes
  Have excellent error-correction abilities that outperform many other codes
  digital video broadcasting, 10Gbps Ethernet, power-line network, latest version of 802.11

## Slide 38: Error-Detecting Codes
Linear, systematic block codes
  Parity
  Checksums
  Cyclic Redundancy Checks (CRCs)

## Slide 39: Parity (1)
Parity bit is added as the modulo 2 sum of data bits
  Equivalent to XOR; this is even parity
  Ex: 1110000  11100001
  Detection checks if the sum is wrong (an error)
Simple way to detect an odd number of errors
  Ex: 1 error, 11100101; detected, sum is wrong
  Ex: 3 errors, 11011001; detected sum is wrong
  Ex: 2 errors, 11101101; not detected, sum is right!
  Error can also be in the parity bit itself
  Random errors are detected with probability ½

## Slide 40: Parity (2)
Interleaving of N parity bits detects burst errors up to N
  Each parity sum is made over non-adjacent bits
  An even burst of up to N errors will not cause it to fail

## Slide 41: Checksums
Checksum is an error-detecting technique that can be applied to a message of any length.
Checksum treats data as N-bit words and adds N check bits that are the modulo 2N sum of the words
  Ex: Internet 16-bit 1s complement checksum
Properties:
  Improved error detection over parity bits
  Detects bursts up to N errors
  Vulnerable to systematic errors, e.g., added zeros

## Slide 42: Checksum

## Slide 43: Checksum Example
Suppose the message is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers.
For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers.
The decimal number 36 in binary is (100100)2. To change it to a 4-bit number we add the extra leftmost bit to the right four bits as shown below.

## Slide 44: Checksum Example (cont.)
The sender adds all five numbers in one’s complement to get the sum = 6. The sender then complements the result to get the checksum = 9, which is 15 − 6.
Note that 6 = (0110)2 and 9 = (1001)2; they are complements of each other.
The sender sends the five data numbers and the checksum (7, 11, 12, 0, 6, 9).
If there is no corruption in transmission, the receiver receives (7, 11, 12, 0, 6, 9) and adds them in one’s complement to get 15.

## Slide 45: Calculation procedure of the previous example

## Slide 46: Procedure to calculate the traditional checksum

## Slide 47: Algorithm to calculate the traditional checksum

## Slide 48: Problems of the traditional checksum calculation
If two 16-bit items are transposed in transmission, the checksum cannot catch this error.
The reason is that the traditional checksum is not weighted: it treats each data item equally.
In other words, the order of data items is immaterial to the calculation.
Several approaches have been used to prevent this problem, such as Fletcher and Adler.
Notes: Immaterial:无关紧要的

## Slide 49: Algorithm to calculate an 8-bit Fletcher checksum
Weight each data item according to its position
The 8-bit Fletcher is calculated over data octets(bytes) and creates a 16-bit checksum
The calculation is done modulo 256.
Two accumulators: L and R

## Slide 50: Algorithm to calculate an Adler checksum
Similar to the 16-bit Fletcher with three differences:
  Calculation is done on single bytes instead of 2 bytes at a time.
  The modulus is a prime number(65521) instead of 65536.
  R is initialized to 1 instead of 0.
Notes: 旨在改进 Fletcher Checksum。Adler校验和使用质数作为模数，比如251（Fletcher 256）， 65521（Fletcher 65536）

## Slide 51: Cyclic codes
Cyclic codes are special linear block codes with one extra property.
In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
For example, if 1011000 is a codeword and we cyclically left-shift, then 0110001 is also a codeword.
Cyclic Redundancy Check (CRC), which is used in networks such as LANs and WANs. It adds bits so that transmitted frame viewed as a polynomial is evenly divisible（整除） by a generator polynomial.

## Slide 52: A polynomial to represent a binary word

## Slide 53: CRC Calculation
校验码的生成过程：假设要发送的信息用多项式 C(x) 表示，将 C(x) 左移 R 位（可表示成 C(x) << R），这样 C(x) 的右边就会空出 R 位，这就是校验码的位置。用 C(x) << R除以 G(x) 得到的余数就是校验码。
  G(x)： 表示 CRC 的生成多项式，是接收方和发送方的一个约定，由 CRC 规范给定。在整个传输过程中，这个二进制数始终保持不变。例如 CRC-CCITT 的生成多项式为 G(x) = x16 + x12 + x5 + 1。
  C(x)： 表示发送的原始数据的多项式。例如 C(x) = x5 + x3 + x2 + x + 1 表示发送的数据为 101111
  R(x)： 表示CRC 码的多项式。R(x) = (C(x) << R) % G(x)
  T(x)： 表示发送的原始数据加上 CRC 码之后的多项式。T(x) = C(x) << R + R(x)
  K：发送数据的长度。其等于 C(x) 中的最高次的幂 + 1。如上例子的 C(x) 中，K = 5 + 1 = 6
  R： CRC 码 的长度。CRC校验码位数 = 生成多项式G(x)位数 - 1。
101000110100000
110101
01110
1101010110
原始数据C(x)
G(x)除数
商（CRC不用）
左移R位，补位0
CRC码R(x)
被除数C(x)<<R
实际需要发送的数据是101000110101110。需要注意的是，余数（R(x)）不足 R 位时，高位补 0！
Notes: CRC分为以下几种标准：
CRC-12码
CRC-16码
CRC-CCITT码
CRC-32码
CCITT国际电报电话咨询委员会，是国际电信咨询机构，简称CCITT,总部设在瑞士日内瓦

## Slide 54: CRC division using polynomials

## Slide 55: Example Calculation of the CRC
Start by adding 0s to frame and try dividing
Offset by any reminder to make it evenly divisible

## Slide 56: Division in CRC encoder

## Slide 57: Division in the CRC decoder for two cases

## Slide 58: Performance
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
A generator that contains a factor of x + 1 can detect all odd-numbered errors.

## Slide 59: Performance (contd.)
All burst errors with L ≤ r will be detected.
All burst errors with L = r + 1 will be detected with probability 1 – (1/2)r–1.
All burst errors with L > r + 1 will be detected with probability 1 – (1/2)r.

## Slide 60: Example
Solution
a. No xi can be divisible by x + 1. in other words, xi /(x + 1) always has a remainder. Any single-bit error can be caught.
b. If i is equal to or greater than 3, xi is divisible by g(x). The remainder of xi /x3 is zero. All single-bit errors in positions 1 to 3 are caught.
c. All values of i make xi divisible by g(x). No single-bit error can be caught. This g(x) is useless.
Which of the following g(x) values guarantees that a single-bit error is caught? For each case, what is the error that cannot be caught?
a. x + 1 b. x3 c. 1

## Slide 61: Properties of Good Polynomials
A good polynomial generator needs to have the following characteristics:
It should have at least two terms.
The coefficient of the term x0 should be 1.
It should have the factor x + 1.

## Slide 62: CRC: a good candidate for many networks
Based on standard polynomials:
  Ex: Ethernet 32-bit CRC is defined by:
  Computed with simple shift/XOR circuits
Stronger detection than checksums:
  very good performance in detecting single-bit errors, double errors, an odd number of errors, and burst errors.
  Not vulnerable to systematic errors

## Slide 63: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 64: Elementary Data Link Protocols
Assumptions underly the communication model
Three simplex link-layer protocols
  Utopia: No Flow Control or Error Correction
  Adding Flow Control: Stop-and-Wait
  Adding Error Correction: Sequence Numbers and ARQ

## Slide 65: Initial Simplifying Assumptions (1 of 2)
Independent processes
  Physical, data link, and network layers are independent
  Communicate by passing messages back and forth
Unidirectional communication
  Machines use a reliable, connection-oriented service
Reliable machines and processes
  Machines do not crash

## Slide 66: Initial Simplifying Assumptions (2 of 2)
Implementation of the physical, data link, and network layers
The physical layer process and some of the data link layer process run on dedicate hardware called a NIC (Network Interface Card).
The rest of the link layer process and the network layer process run on the main CPU as part of the operating system, with the software for the link layer process often taking the form of a device driver.
However, other implementations are also possible (e.g., three processes offloaded to dedicated hardware called a network accelerator)

## Slide 67: Basic Transmission And Receipt (1 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 68: Basic Transmission And Receipt (2 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 69: Basic Transmission And Receipt (3 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 70: Basic Transmission And Receipt (4 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 71: Basic Transmission And Receipt (5 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h … continued on the next slide

## Slide 72: Basic Transmission And Receipt (6 of 6)
Some definitions needed in the protocols to follow. These definitions are located in the file protocol.h (end of code)

## Slide 73: Simplex Link-Layer Protocols
Utopia: No Flow Control or Error Correction
Adding Flow Control: Stop-and-Wait
Adding Error Correction: Sequence Numbers and ARQ

## Slide 74: Utopian Simplex Protocol (1)
A utopian simplex protocol … continued on the next slide
  Assumes no errors, and receiver as fast as sender
  Considers one-way data transfer
  That’s it, no error or flow control …
    This is essentially what Ethernet does – just blast packets and receive as quickly as possible

## Slide 75: Utopian Simplex Protocol (2)
A utopian simplex protocol … continued on the next slide

## Slide 76: Utopian Simplex Protocol (3)
A utopian simplex protocol (end of code)

## Slide 77: Utopian Simplex Protocol (4)

## Slide 78: Stop-and-Wait – Error-free channel (1)
A simplex stop-and-wait protocol … continued on the next slide
Protocol (p2) ensures sender can’t outpace receiver:
  Receiver returns a dummy frame (ack) when ready
  Only one frame out at a time – called stop-and-wait
  We added flow control!

## Slide 79: Stop-and-Wait – Error-free channel (2)
A simplex stop-and-wait protocol … continued on the next slide
Sender waits to for ack after passing frame to physical layer.

## Slide 80: Stop-and-Wait – Error-free channel (3)
A simplex stop-and-wait protocol (end of code)
Receiver sends ack after passing frame to network layer.

## Slide 81: Stop-and-Wait – Noisy channel (1)
A positive acknowledgement with retransmission protocol … continued on the next slide
ARQ (Automatic Repeat reQuest) adds error control
  ARQ is also called PAR (Positive Acknowledgement with Retransmission)
  Receiver acks frames that are correctly delivered
  Sender sets timer and resends frame if no ack)
For correctness, frames and acks must be numbered
  Else receiver can’t tell retransmission (due to lost ack or early timer) from new frame
  For stop-and-wait, 2 numbers (1 bit) are sufficient

## Slide 82: Stop-and-Wait – Noisy channel (2)
A positive acknowledgement with retransmission protocol … continued on the next slide
This is essentially what 802.11 does – stop-and-wait to handle wireless errors. 802.11 uses a larger sequence number (12 bits) and gives up after a limited number of retransmissions (retries).

## Slide 83: Stop-and-Wait – Noisy channel (3)
A positive acknowledgement with retransmission protocol (end of code)

## Slide 84: Stop-and-Wait – Noisy channel (4)
Sender sends frame with CRC, and sets timer,
Receiver verifies CRC value and sends ACK,
Sender sends a new frame when receives an ACK, sends old frame when timeout.

## Slide 85: Stop-and-Wait – Noisy channel (5)
The 1st frame is sent and acknowledged.
The 2nd frame is sent, but lost. After time-out, it is resent.
The 3rd frame is sent and ACKed, but the ACK is lost. The frame is resent.
It is not right for the network layer at the receiver site receives two copies of the 3rd frame.
Is there any problem here?
How to correct this problem?
Using sequence numbers and acknowledgment numbers.

## Slide 86: Stop-and-Wait – Noisy channel (6)
Adding sequence numbers and acknowledgment numbers to prevent duplicates.
The 1st frame is sent and acknowledged.
The 2nd frame is sent, but lost. After time-out, it is resent.
The 3rd frame is sent and ACKed, but the ACK is lost. The frame is resent.

## Slide 87: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 88: Improving Efficiency
Need bidirectional data transmission
Link layer efficiency improvement
  Send multiple frames simultaneously before receiving an acknowledgement

## Slide 89: Piggybacking
Bidirectional transmission: piggybacking
  Use the same link for data in both directions
  Interleave data and control frames on the same link
  Temporarily delay outgoing acknowledgements so they can be hooked onto the next outgoing data frame
Piggybacking advantages
  A better use of the available channel bandwidth
  Lighter processing load at the receiver
Piggybacking issue
  Determining time data link layer waits for a packet to piggyback the acknowledgement
Notes: If the data link layer waits longer than the sender’s timeout period, the frame will be retransmitted.

## Slide 90: Multiple Frames in Flight
Three bidirectional sliding window protocols
  One-bit sliding window, go-back-n, selective repeat
Consider any instant of time
  Sender maintains a set of sequence numbers corresponding to frames it is permitted to send. Frames are said to fall within the sending window
  Receiver maintains a receiving window corresponding to the set of frames it is permitted to accept
Differ among themselves in terms of efficiency, complexity, and buffer requirements

## Slide 91: Sliding Window Concept
Sending window
  Sender maintains window of frames it can send
  Needs to buffer them for possible retransmission
  Window advances with next acknowledgements
Receiving window
  Receiver maintains window of frames it can receive
  Needs to keep buffer space for arrivals
  Window advances with in-order arrivals

## Slide 92: Sliding window in circular format
Window size: 7
Sequence number: 4-bit

## Slide 93: Sliding window in linear format

## Slide 94: Sliding Window Example
A sliding window advancing at the sender and receiver
  Ex: window size is 1, with a 3-bit sequence number.
At the start
After the first frame has been sent
After the first frame has been received
After the first acknowledgement has been received
Sender
Receiver

## Slide 95: Pipelining
Larger windows enable pipelining for efficient link use
  Stop-and-wait (w=1) is inefficient for long links
  Best window (w) depends on bandwidth-delay (BD)
  Want w = 2BD+1 to ensure high link utilization
  Notice: BD here is in the number of frames
  If we use BDP directly, suppose L is the length of a frame, the formula should be w = 2BDP/L+1
Pipelining leads to different choices for errors/buffering
  We will consider Go-Back-N and Selective Repeat
Link utilization =
D
L/B
D
ACK
F1
F2
…
Sender
Receiver
F3
Fn
Notes: Pipelining means that there are multiple frames outstanding in the network at any instant.
For stop-and-wait, imagine a link from Seattle to Amsterdam that has a 500ms round-trip time. It doesn’t matter how fast the link is in bits/sec, stop-and-wait will only let it run at two packets per second.

## Slide 96: Link Utilization without Pipelining
Link utilization =
D
L/B
D
ACK
F1
Sender
Receiver
F2
Stop-and-wait
Stop-and-wait with ACK piggybacking
D
L/B
D
F with ACK
F1
Sender
Receiver
F2
L/B
Link utilization =

## Slide 97: Link Utilization with Pipelining
Link utilization =
D
L/B
D
ACK
F1
F2
…
Sender
Receiver
F3
Fn
…
D
L/B
D
ACK
F1
F2
…
Sender
Receiver
F3
Fn
…
L/B
Link utilization =
ACK piggybacking
individual short ACK

## Slide 98: Pipelining Example
E.g.: For a link with a bandwidth of 50kbps and a one-way transmit time of 250msec, the bandwidth-delay product is 12.5 kbits or 12.5 frames of 1000bits each.
2BD+1 = 2 * 12.5 + 1 = 26 frames
At t = 0 ms, the sender begins sending frame 0 and sends a new frame every 20 msec.
At t = 520 ms, it has finished sending 26 frames, and the acknowledgement for frame 0 will have just arrived.
Thereafter, acknowledgements will arrive every 20 msec, so the sender will always get permission to continue just when it needs it.
From then onwards, 25 or 26 unacknowledged frames will always be outstanding. Put in other terms, the sender’s maximum window size is 26.

## Slide 99: One-Bit Sliding Window (1)
A 1-bit sliding window protocol … continued on the next slide
The sequence numbers are based on modulo-2 arithmetic.
Transfers data in both directions with stop-and-wait
      Piggybacks acks on reverse data frames for efficiency
      Handles transmission errors, flow control, early timers
      Window size = 1

## Slide 100: One-Bit Sliding Window (2)
A 1-bit sliding window protocol … continued on the next slide

## Slide 101: One-Bit Sliding Window (3)
A 1-bit sliding window protocol (end of code)

## Slide 102: One-Bit Sliding Window (4)
Two scenarios for protocol 4. (a) Normal case. (b) Abnormal case. The notation is (seq, ack, packet number). An asterisk indicates where a network layer accepts a packet.
Abnormal
Normal
simultaneous start
duplicate transmissions
correct but slow

## Slide 103: Pipelining and error recovery
Effect of an error when (a) receiver’s window size is 1 and (b) receiver’s window size is large.
Go-Back-N
Selective Repeat

## Slide 104: Go-Back-N
Receiver only accepts/acks frames that arrive in order
  Discards frames that follow a missing/errored frame
  Sender times out and resends all outstanding frames
Tradeoff made for Go-Back-N:
  Simple strategy for receiver; needs only 1 frame
  Wastes link bandwidth for errors with large windows; entire window is retransmitted
Receiver’s window size is always 1
Sender’s window must be less than 2m
Cumulative Acknowledgment: Ack for frame n means n - 1, n - 2, and so on are also acknowledged.

## Slide 105: Send window for Go-Back-N
The send window is an abstract concept defining an imaginary box of size 2m − 1 with three variables: Sf, Sn, and Ssize.
The send window can slide one or more slots when a valid acknowledgment arrives.

## Slide 106: Receive window for Go-Back-N
The receive window is an abstract concept defining an imaginary box of size 1 with one single variable Rn.
The window slides when a correct frame has arrived; sliding occurs one slot at a time.

## Slide 107: Send Window size for Go-Back-N

## Slide 108: FSMs for Go-Back-N Protocol

## Slide 109: Cumulative Acknowledgment
Although ACK 2 is lost, ACK 3 serves as both ACK 2 and ACK 3.

## Slide 110: What happens when a frame is lost in Go-Back-N?
The receiver receives frames 2 and 3, but they are discarded because they are received out of order.
Notes: Frames 0, 1, 2, and 3 are sent. However, frame 1 is lost. The receiver receives frames 2 and 3, but they are discarded because they are received out of order. The sender receives no acknowledgment about frames 1, 2, or 3. Its timer finally expires. The sender sends all outstanding frames (1, 2, and 3) because it does not know what is wrong. Note that the resending of frames 1, 2, and 3 is the response to one single event.

## Slide 111: Simulation of multiple timers in software
(a) The queued timeouts. (b) The situation after the first timeout has expired.

## Slide 112: Go-Back-N protocol (1)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 113: Go-Back-N protocol (2)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 114: Go-Back-N protocol (3)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 115: Go-Back-N protocol (4)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 116: Go-Back-N protocol (5)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 117: Go-Back-N protocol (6)
A sliding window protocol using go-back-n … continued on the next slide

## Slide 118: Go-Back-N protocol (7)
A sliding window protocol using go-back-n (end of code)

## Slide 119: Selective Repeat
Receiver accepts frames anywhere in receive window
  Cumulative ack indicates highest in-order frame
  NAK (negative ack), sent immediately when a error may happened, causes sender retransmission of a missing frame before a timeout resends window
The size of the sender and receiver window must be at most 2m-1.
Tradeoff made for Selective Repeat:
  More complex than Go-Back-N due to buffering at receiver and multiple timers at sender
  More efficient use of link bandwidth as only lost frames are resent (with low error rates)

## Slide 120: Send and receive window for Selective Repeat

## Slide 121: Window size for Selective Repeat

## Slide 122: Window size for Selective Repeat (cont.)
For correctness, we require:
  Sequence numbers (s) at least twice the window (w)
Originals
Originals
Retransmits
Retransmits
Error case (s=8, w=7) – too few sequence numbers
Correct (s=8, w=4) – enough sequence numbers
New receive window overlaps old – retransmits ambiguous
New and old receive window don’t overlap – no ambiguity
Initial situation with a window of size 7
After 7 frames have been sent and received but not acknowledged.
Initial situation with a window size of 4.
After 4 frames have been sent and received but not acknowledged

## Slide 123: FSMs for Selective Repeat Protocol

## Slide 124: What happens when a frame is lost in Selective Repeat?
The timers need to be numbered.
distinguish between the acceptance of a frame and its delivery to the network layer.
A NAK is sent once for each window position and defines the first slot in the window.
Cumulative acknowledgment
Notes: There are two conditions for the delivery of frames to the network layer:
First, a set of consecutive frames must have arrived.
Second, the set starts from the beginning of the window.

## Slide 125: Selective Repeat Protocol (1)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 126: Selective Repeat Protocol (2)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 127: Selective Repeat Protocol (3)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 128: Selective Repeat Protocol (4)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 129: Selective Repeat Protocol (5)
A sliding window protocol using selective repeat … continued on the next slide

## Slide 130: Selective Repeat Protocol (6)
A sliding window protocol using selective repeat (end of code)

## Slide 131: Exercises
Assume a sender sends 6 frames: frames 0, 1, 2, 3, 4, and 5. The sender receives an ACK with ackNo = 3.
What is the interpretation if the system is using GBN or SR?
Solution
If the system is using GBN, it means that frames 0, 1, and 2 have been received uncorrupted and the receiver is expecting frame 3.
If the system is using SR, it means that frame 3 has been received uncorrupted; the ACK does not say anything about other frames.

## Slide 132: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 133: Data Link Protocols in Practice
HDLC (High-level Data Link Control )
Packet over SONET
ADSL (Asymmetric Digital Subscriber Loop)

## Slide 134: HDLC
High-level Data Link Control (HDLC) is a bit-oriented protocol for communication over point-to-point and multipoint links.
Although HDLC is more a theoretical issue than practical, most of the concept defined in HDLC is the basis for other practical protocols such as PPP, Ethernet, or wireless LANs.
HDLC provides two common transfer modes that can be used in different configurations: normal response mode (NRM) and asynchronous balanced mode (ABM).

## Slide 135: Normal Response Mode (NRM)
In NRM, the station configuration is unbalanced.
  We have one primary station and multiple secondary stations.
  A primary station can send commands; a secondary station can only respond.
The NRM is used for both point-to-point and multipoint links

## Slide 136: Asynchronous Balanced Mode
In ABM, the configuration is balanced.
The link is point-to-point, and each station can function as a primary and a secondary (acting as peers),

## Slide 137: HDLC Frames
HDLC defines three types of frames:
  information frames (I-frames): to transport data-link user data and control information relating to user data (piggybacking)
  supervisory frames (S-frames): to transport control information
  unnumbered frames (U-frames): reserved for system management
HDLC Frame formats and their control fields
Flag: 01111110

## Slide 138: Example of connection and disconnection
SABM: set asynchronous balanced mode
UA: unnumbered acknowledgment
DISC: disconnect
Notes: how U-frames can be used for connection establishment and connection release.
Node A asks for a connection with a set asynchronous balanced mode (SABM) frame; node B gives a positive response with an unnumbered acknowledgment (UA) frame. After these two exchanges, data can be transferred between the two nodes (not shown in the figure). After data transfer, node A sends a DISC (disconnect) frame to release the connection; it is confirmed by node B responding with a UA (unnumbered acknowledgment).

## Slide 139: Example of piggybacking with and without error
RR: Receive ready
REJ: Reject

## Slide 140: Packet over SONET
Packet over SONET. (a) A protocol stack. (b) Frame relationships.
Packet over SONET is the method used to carry IP packets over SONET optical fiber links
  Uses PPP (Point-to-Point Protocol) for framing

## Slide 141: Point-to-Point Protocol
PPP (Point-to-Point Protocol) is a general method for delivering packets across links
  Framing uses a flag (0x7E) and byte stuffing
  “Unnumbered mode” (connectionless unacknowledged service) is used to carry IP packets
  Errors are detected with a checksum
  Separate packets, error detection
  Link Control Protocol (LCP)
  Network Control Protocol (NCP)
IP packet
0x21 for IPv4
The PPP full frame format for unnumbered mode operation

## Slide 142: Differences between PPP and HDLC
Framing
  PPP is byte oriented. PPP uses byte stuffing and all frames are an integral number of bytes.
  HDLC is bit oriented. HDLC uses bit stuffing and allows frames of, for example, 30.25 bytes.
Services
  PPP always use an ‘‘unnumbered mode’’ to provide connectionless unacknowledged service used in the Internet. PPP can also provide reliable transmission in noisy environments, such as wireless networks (rare in practice).
  HDLC provides reliable transmission with a sliding window, acknowledgements, and timeouts in the manner we have studied.

## Slide 143: State machine for link control in PPP
A link control protocol brings the PPP link up/down
State machine for link control

## Slide 144: Multiplexing in PPP
Although PPP is a link-layer protocol, it uses another set of protocols to establish the link, authenticate the parties involved, and carry the network-layer data.
Three sets of protocols are defined to make PPP powerful: the Link Control Protocol (LCP), two Authentication Protocols (APs), and several Network Control Protocols (NCPs).
PAP（Password Authentication Protocol）
CHAP（Challenge Handshake Authentication Protocol）

## Slide 145: LCP packet encapsulated in a frame

## Slide 146: PAP packets encapsulated in a PPP frame

## Slide 147: CHAP packets encapsulated in a PPP frame

## Slide 148: IPCP packet encapsulated in a PPP frame
IPCP: Internet Protocol Control Protocol

## Slide 149: An example of PPP

## Slide 150: ADSL (1 of 2)
ADSL protocol stacks
Widely used for broadband Internet over local loops
  ADSL runs from modem (customer) to DSLAM (ISP)
  IP packets are sent over PPP and AAL5/ATM (over)

## Slide 151: ADSL (2 of 2)
PPP data is sent in AAL5 frames over ATM cells:
  ATM is a link layer that uses short, fixed-size cells (53 bytes); each cell has a virtual circuit identifier
  AAL5 is a format to send packets over ATM
  PPP frame is converted to a AAL5 frame (PPPoA)
AAL5 frame is divided into 48 byte pieces, each of which goes into one ATM cell with 5 header bytes
Notes: Re ATM: ATM was a major technology in the 1990s that was hyped to win in the convergence of the Internet and telecommunications, but IP won instead. The short, fixed-size cells give flexibility (can mix voice and data without having the voice wait for a whole data packet). ATM is now used in niches such as ADSL and WAN links.

## Slide 152: Data Over Cable Service Interface Specification (DOCSIS)
DOCSIS Frame to codeword mapping

## Slide 153: The Data Link Layer Chapter 3
Data Link Layer Design Issues
Error Detection and Correction
Elementary Data Link Protocols
Improving Efficiency
Data Link Protocols in Practice
Summary

## Slide 154: Summary (1 of 4)
The task of the data link layer is
  to convert the raw bit stream offered by the physical layer into a stream of frames for use by the network layer. Various framing methods are used, including byte count, byte stuffing, and bit stuffing.
  to present this stream with varying levels of reliability: connectionless, unacknowledged service to reliable, connection-oriented service.
Data link protocols can provide
  error control to detect or correct damaged frames and to retransmit lost frames.
  flow control to prevent a fast sender from overrunning a slow receiver.
  The sliding window mechanism is widely used to integrate error control and flow control in a simple way. When the window size is 1 packet, the protocol is stop-and-wait.

## Slide 155: Summary (2 of 4)
Codes for error correction and detection add redundant information to messages by using a variety of mathematical techniques.
  Convolutional codes and Reed-Solomon codes are widely deployed for error correction, with low-density parity check codes increasing in popularity.
  The codes for error detection that are used in practice include cyclic redundancy checks and checksums.
  All these codes can be applied at the link layer, as well as at the physical layer and higher layers.

## Slide 156: Summary (3 of 4)
A series of protocols that provide a reliable link layer using acknowledgements and retransmissions, or ARQ (Automatic Repeat reQuest), under more realistic assumptions.
  an error-free environment in which the receiver can handle any frame sent to it,
  we introduced flow control, followed by error control with sequence numbers and the stop-and-wait algorithm.
  Then we used the sliding window algorithm to allow bidirectional communication and introduce the concept of piggybacking.
  The last two protocols pipeline the transmission of multiple frames to prevent the sender from blocking on a link with a long propagation delay.
    The receiver can either discard all frames other than the next one in sequence (go-back-n), or buffer out-of-order frames and send negative acknowledgements for greater bandwidth efficiency (selective repeat ).

## Slide 157: Summary (4 of 4)
The Internet uses PPP as the main data link protocol over point-to-point lines.
  It provides a connectionless unacknowledged service, using flag bytes to delimit frames and a CRC for error detection.
  It is used to carry packets across a range of links, including SONET links in wide area networks and ADSL links for the home.
DOCSIS is used when Internet service is provided over the existing cable TV network.

## Slide 158: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.