## Slide 1: COMPUTER NETWORKS
Chapter 4 The Medium Access Control Sublayer

## Slide 2: The MAC Sublayer
Responsible for deciding who sends next on a multi-access link
  An important part of the link layer, especially for LANs
Physical
Link
Network
Transport
Application
MAC is in here!

## Slide 3: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 4: The Channel Allocation Problem
Static channel allocation
Assumptions for dynamic channel allocation

## Slide 5: Multiple Access Problem
An example: a classroom
Human protocols:
  “Give everyone a chance to speak”
  “Don’t speak until you are spoken to”
  “Don’t monopolize the conversation”
  “Raise your hand if you have a question”
  “Don’t interrupt when someone is speaking”
  “Don’t fall asleep when someone else is talking”
  In LANs, WiFi, satellite networks, cocktail party
  If more than 2 users send at the same time - collision
  All collided packets are lost -> waste of bandwidth
Notes: 鸡尾酒会问题(Cocktail Party Problem)最早是由英国认知科学家Edward Colin Cherry于1953年在研究选择注意机制时提出的一个著名问题, 该问题是说人可以在复杂听觉环境下很容易地将注意力集中在某一个感兴趣的声音刺激上并忽略其它背景声音, 而计算听觉模型却受噪音影响严重.

## Slide 6: Static Channel Allocation
Static allocation
  For fixed channel and traffic from N users
  Divide up bandwidth using FDM, TDM, CDMA, etc.Poor fit to computer systems with extremely bursty data traffic
  Performance affected when peak traffic to mean traffic ratios are 1000:1
  Most channels will be idle most of the time
Dynamic allocation tries to resolve static allocation problems
  gives the channel to a user when they need it.

## Slide 7: Assumptions for Dynamic Channel Allocation
Independent traffic
Single channel
Observable collisions
Continuous or slotted time
Carrier sense or no carrier sense

## Slide 8: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 9: Multiple Access Protocols
ALOHA
Carrier Sense Multiple Access
Collision-free protocols
Limited-contention protocols
Wireless LAN protocols

## Slide 10: ALOHA
Pure ALOHA
Slotted ALOHA

## Slide 11: ALOHA Network
Developed by Norm Abramson at the Univ. of Hawaii
  the guy had interest in surfing and packet switching
  mountainous islands → land-based network difficult to install
  fully decentralized protocol
ACK
ACK
ACK
ACK
ALOHA(Additive Link On-Line Hawaii system)
Notes: ALOHA(Additive Link On-Line Hawaii system)

## Slide 12: Pure ALOHA
In pure ALOHA, frames are transmitted at completely arbitrary times.
Users transmit frames whenever they have data
Users retry after a random time for collisions
  Efficient and low-delay under low load
传输之前不侦听信道
即使少量重叠，两帧也彻底破坏
想说就说

## Slide 13: Vulnerable Period（冲突危险周期）
Vulnerable period for the shaded frame
Collisions happen when other users transmit during a vulnerable period that is twice the frame time
  Synchronizing senders to slots can reduce collisions
Frame time（帧时）: the frame length divided by the bit rate

## Slide 14: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps.
What is the requirement to make this frame collision-free?
Solution
Frame time is 200 bits/200 kbps or 1 ms.
The vulnerable time is 2 × 1 ms = 2 ms.
This means no station should send later than 1 ms before this station starts transmission and no station should start sending during the period (1ms) that this station is sending.

## Slide 15: Channel Utilization (1)
Assumption: An infinite collection of users; Fixed-length frame
New frames generated by the stations are modeled by a Poisson distribution with a mean of frames per frame time.
  For reasonable throughput,
The old (retransmitted) and new frames combined are modeled by a Poisson distribution with a mean of frames per frame time.
Throughput per frame time S = GP0,
  P0 is the probability of a transmission succeeding ---- a frame does not suffer a collision.

## Slide 16: Channel Utilization (2)
The probability that frames are generated during a frame time, in which frames are expected, is given by the Poisson distribution
The mean number of frames generated in the vulnerable period (an interval two frame times long):
The probability of no frames being initiated during the entire vulnerable period:
Throughput:
  maximum at with
P0 = 成功传输1帧的概率
= 冲突危险周期（2个帧时） 内没有帧的概率
= =

## Slide 17: Example
A pure ALOHA network transmits 200-bit frames on a shared channel of 200 kbps.
What is the throughput if the system (all stations together) produces
a. 1000 frames per second?
b. 500 frames per second?
c. 250 frames per second?

## Slide 18: Solution
The frame time is 200 bits/200 kbps or 1 ms.
a. If the system creates 1000 frames per second, or 1 frame per millisecond, then G = 1. In this case S = G × e−2G = 0.135 (13.5%). This means that the throughput is 1000 × 0.135 = 135 frames. Only 135 frames out of 1000 will probably survive.
b. If the system creates 500 frames per second, or 1/2 frames per millisecond, then G = 1/2. In this case S = G × e−2G = 0.184 (18.4%). This means that the throughput is 500 × 0.184 = 92. Only 92 frames out of 500 will probably survive.
c. If the system creates 250 frames per second, or 1/4 frames per millisecond, then G = 1/4. In this case S = G× e−2G = 0.152 (15.2%). This means that the throughput is 250 × 0.152 = 38. Only 38 frames out of 250 will probably survive

## Slide 19: Slotted ALOHA
  将时间分为以一个帧时为单位的离散的时间片，每个时间片可以用来发送一个帧。站点有数据发送时，必须等到时间片的开始才能发送
    Low load wastes slots, high loads causes collisions. Requires sync of clocks
    Applied in Internet access over cable, multiple RFID tags talk to the same RFID reader
Slotted ALOHA is twice as efficient as pure ALOHA
  Vulnerable period = 1个帧时。P0 = e-G ,S = Ge-G
  Throughput: maximum at G = 1 with S = 1/e (about 0.368)
P0 = 成功传输1帧的概率 = 冲突危险周期（1个帧时）内没有帧的概率 = =

## Slide 20: Throughput versus offered traffic
Throughput versus offered traffic for ALOHA systems
Operating at higher values of G reduces the number of empties but increases the number of collisions exponentially. For slotted ALOHA systems,
As a result of the exponential dependence of E upon G, small increases in the channel load can drastically reduce its performance.

## Slide 21: Example
Measurement of a slotted ALOHA channel with an infinite number of users show that 20 percent of slots are idle .
a) What is the channel load, G?
b) What is the throughput?
c) Is the channel underloaded or overloaded?
a) Poisson distribution: Pr[k] = Gke-G/k!
    P0 = e-G = 0.2, so G = -lnP0 = -ln 0.2 = 1.6
b) S = G*e-G = G*0.2 = 1.6*0.2 = 0.32
c) G = 1.6 > 1, so the channel is overloaded.

## Slide 22: Carrier Sense Multiple Access Protocols
Persistent and nonpersistent CSMA
  1-persistent CSMA (Carrier Sense Multiple Access)
  Nonpersistent CSMA
  p-persistent CSMA
CSMA with collision detection
  Known as CSMA/CD (CSMA with Collision Detection)
  Basis of the classic Ethernet LAN

## Slide 23: CSMA
CSMA improves on ALOHA by sensing the channel!
  User doesn’t send if it senses someone else
  Based on the principle “sense before transmit” or “listen before talk.”
讲前先听
Notes: 802.11 uses a refinement of p-persistent CSMA

## Slide 24: Behavior of three persistence methods
Variations on what to do if the channel is busy:
  1-persistent (greedy) sends as soon as idle
  Nonpersistent waits a random time then tries again
  p-persistent sends with probability p when idle

## Slide 25: 1-persistent CSMA
When a station has data to send, it first listens to the channel to see if anyone else is transmitting at that moment.
  If the channel is idle, the stations sends its data. (with a probability of 1)
  if the channel is busy, the station just waits until it becomes idle (persistent). Then the station transmits a frame.
  If a collision occurs, the station waits a random amount of time and starts all over again.
冲突的两种可能情景：
  1.信号传播延迟造成的冲突；如第一个站的信号还没到达第二个站，第二个站则会认为信道空闲，会立即发送数据；
  2.多个站点同时监听到信道空闲，同时发送。

## Slide 26: Nonpersistent CSMA
A station senses the channel when it wants to send a frame,
  if no one else is sending, the station begins doing so itself.
  if the channel is already in use, the station does not continually sense it (nonpersistent). Instead, it waits a random period of time and then repeats the algorithm.
Better channel utilization but longer delays than 1-persistent CSMA.

## Slide 27: p-persistent CSMA
When a station becomes ready to send, it senses the channel.
  If it is idle, it transmits with a probability p. With a probability q = 1 − p, it defers until the next slot.
  If that slot is also idle, it either transmits or defers again, with probabilities p and q. This process is repeated until either the frame has been transmitted or another station has begun transmitting.
It applies to slotted channels.
IEEE 802.11 uses a refinement of p-persistent CSMA
概率p：降低1-persistent CSMA中多个站点同时发送而造成冲突的概率
坚持监听：克服non-persistent CSMA中造成的时间延迟
p的选择直接关系到协议的性能

## Slide 28: Flow diagram for three persistence methods

## Slide 29: Persistent and Nonpersistent CSMA
Comparison of the channel utilization versus load for various random access protocols
CSMA outperforms ALOHA, and being less persistent is better under high load.
“先听后发”机制在发送过程中如果发生冲突，仍要将剩余的无效数据发送完，浪费时间和带宽。

## Slide 30: CSMA with Collision Detection (1)
CSMA/CD improvement is to detect/abort collisions
  A station monitors the medium after it sends a frame to see if the transmission was successful.
  冲突检测：通过检测回复信号的能量或者脉冲宽度并将之与发送的信号做比较，如果信号不同，就可以判断发生冲突。
发送前监听信道，若闲则发送数据；若忙则一直监听信道直至空闲，开始发送数据；
发送数据时边发送边监听信道，若未检测到冲突，则发送完成。一旦检测到冲突，立即停止发送数据，发送一串阻塞信号（jamming signal），并等待一随机时间后再重新尝试发送。
Notes: jamming signal：让所有用户都知道现在已经发生了冲突。

## Slide 31: CSMA with Collision Detection (2)
CSMA/CD can be in transmission, contention, or idle state
讲前先听
+
边讲边听
CSMA/CD is the basis of the classic Ethernet LAN.

## Slide 32: Collision of the first bit in CSMA/CD

## Slide 33: Collision and abortion in CSMA/CD

## Slide 34: Flow diagram for CSMA/CD

## Slide 35: Collision Detection
In CSMA/CD,
It is the responsibility of the transmitting station to detect the collision.
To detect the collision in CSMA/CD, each station must follow the condition:
Transmission delay >= 2 * Propagation delay
According to this condition,
Each station must transmit the data packet of size whose transmission delay is at least twice its propagation delay.
If the size of data packet is smaller, then collision detection would not be possible.
Length of Data Packet,
Transmission delay = Length of data packet (L) / Bandwidth (B).
Propagation delay = Distance between the two stations (D) / Propagation speed (V)
We get L / B >= 2 * D / V.
Thus,
L >= 2 * B * D / V

## Slide 36: Example
A network using CSMA/CD has a bandwidth of 10 Mbps. If the maximum propagation time (including the delays in the devices and ignoring the time needed to send a jamming signal) is 25.6 μs, what is the minimum size of the frame?
Solution
The minimum frame transmission time is 2 × Tp = 51.2 μs.
This means, in the worst case, a station needs to transmit for a period of 51.2 μs to detect the collision.
The minimum size of the frame is 10 Mbps × 51.2 μs = 512 bits or 64 bytes.
This is actually the minimum size of the frame for Standard Ethernet, as we will see later in the chapter.

## Slide 37: Collision-Free Protocols
Bit-map protocol
  Basic bit-map method
  Reservation protocols
    The desire to transmit is broadcast before the actual transmission
Token passing
  Token bus
  FDDI (Fiber Distributed Data Interface)
  RPR (Resilient Packet Ring)
    Defined as IEEE 802.17 to standardize the mix of metropolitan area rings in use by ISPs
Binary countdown

## Slide 38: A Bit-Map Protocol
The basic bit-map protocol
Collision-free protocols avoid collisions entirely
  Senders must know when it is their turn to send
The basic bit-map protocol:
  Sender set a bit in contention slot if they have data
  Senders send in turn; everyone knows who has data

## Slide 39: Token Passing
Token ring
The stations in a network are organized in a logical ring. For each station, there is a predecessor and a successor.
The predecessor is the station which is logically before the station in the ring
The successor is the station which is after the station in the ring.
Token sent round ring defines the sending order
  Station with token may send a frame before passing
  Idea can be used without ring too, e.g., token bus

## Slide 40: Binary Countdown
The binary countdown protocol. A dash indicates silence.
Stations send their address in contention slot (log N bits instead of N bits)
Medium ORs bits; stations give up when they send a “0” but see a “1”
Station that sees its full address is next to send

## Slide 41: Limited-Contention Protocols (1 of 2)
Combines the best properties of the contention and collision-free protocols
Limited-contention protocol
  Use contention at low load to provide low delay
  Used a collision-free technique at high load to provide good channel efficiency
  Asymmetric protocols
Review performance of the symmetric protocols first
The adaptive tree-walk protocol

## Slide 42: Limited-Contention Protocols (2 of 2)
Acquisition probability for a symmetric contention channel
Idea is to divide stations into groups within which only a very small number are likely to want to send
  Avoids wastage due to idle periods and collisions
Already too many contenders for a good chance of one winner

## Slide 43: The Adaptive Tree-Walk Protocol
The tree for eight stations
Level 0
Level 1
Level 2
Tree divides stations into groups (nodes) to poll
  Depth first search under nodes with poll collisions
  Start search at lower levels if >1 station expected
At what level in the tree should the search begin?
Each node at level I has a fraction 2-i of the stations below it.
If the number of ready stations is q and uniformly distributed, the mean number of contending stations per slot is 1. i.e., 2-i q = 1
i =log2q
Notes: the expected number of them below a specific node at level i is just 2-i q.
Intuitively, we would expect the optimal level to begin searching the tree to be the one at which the mean number of contending stations per slot is 1. i.e., 2-i q = 1, we can get i =log2q

## Slide 44: Adaptive Tree Walk：Example
Level 0
Level 1
Level 2
A、G要求发送(uniform distributed)
q = 2, i =log2q = log22 = 1
Slot0：冲突（ level0 ，节点1下所有站）；
Slot1：level1左子树(节点2下所有站)，A成功；
Slot2：level1右子树(节点3下所有站)，G成功；
A、C要求发送
Slot0：冲突（ level0 ，节点1下所有站） ；
Slot1：冲突（leve1，节点2下所有站）；
Slot2：level2左子树（节点4下所有站），A成功；
Slot3：level2右子树（节点5下所有站），C成功；
C、D要求发送
Slot0：冲突（ level0 ，节点1下所有站）；
Slot1： level1左子树(节点2下所有站)，冲突；
slot2： level2左子树（节点4下所有站），空闲；
Slot3： level2右子树（节点5下所有站），冲突；
Slot4：左叶子节点，C成功;
Slot5：右叶子节点，D成功;

## Slide 45: Wireless LAN Protocols
Wireless has complications compared to wired.
Nodes may have different coverage regions
  Leads to hidden and exposed terminals
Nodes can’t detect collisions, i.e., sense while sending
  Makes collisions expensive and to be avoided

## Slide 46: Hidden Terminals and Exposed Terminals
A wireless LAN. (a) A and C are hidden terminals when transmitting to B. (b) B and C are exposed terminals when transmitting to A and D.
Hidden terminals: senders that cannot sense each other but nonetheless collide at intended receiver
  Want to prevent;
  loss of efficiency
Exposed terminals: senders who can sense each other but still transmit safely (to different receivers)
  Desirably concurrency;
  improves performance
B  A and C  D

## Slide 47: Wireless LAN Protocols (2 of 2)
The MACA protocol. (a) A sending an RTS to B. (b) B responding with a CTS to A.
发送站点发送请求短帧（RTS）触发接收站点发送应答短帧（CTS），使接收站点周围的站点监听到CTS帧，在一定时间内避免发送数据。
未采用载波侦听机制。
A向B发送RTS（Request To Send）帧，A周围的站点在一定时间内不发送数据，以保证CTS帧返回给A；
B向A回答CTS（Clear To Send）帧，B周围的站点在一定时间内不发送数据，以保证A发送完数据；
A开始发送 –若发生冲突(两站点同时发送RTS)，则等待随机时间，再重试。
Notes: MACA protocol grants access for A to send to B:
  A sends RTS to B [left]; B replies with CTS [right]
  A can send with exposed but no hidden terminals

## Slide 48: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 49: Ethernet (1 of 2)
Classic Ethernet physical layer
Classic Ethernet MAC sublayer protocol
  CSMA/CD with binary exponential backoff
Ethernet performance
Switched Ethernet
Fast Ethernet
802.3
802.3u
802.3z
802.3ae

## Slide 50: Ethernet (2 of 2)
Gigabit Ethernet
10-Gigabit Ethernet
40- and 100-Gigabit Ethernet
Retrospective on Ethernet

## Slide 51: Ethernet
“Dominant” LAN technology developed in the 1970s by Robert Metcalfe and David Boggs.
  First widely used LAN technology
  Simpler, cheaper than token LANs and ATM
  Kept up with speed race: 10, 100, 1000 Mbps 10Gbps, …
Metcalfe’s Ethernet
sketch

## Slide 52: Classic Ethernet Physical Layer
Architecture of classic Ethernet
One shared coaxial cable to which all hosts attached
  Up to 10 Mbps, with Manchester encoding
  Hosts ran the classic Ethernet protocol for access

## Slide 53: Classic Ethernet – Implementation

## Slide 54: Classic Ethernet – 10Base5 and 10Base2

## Slide 55: Classic Ethernet – 10BaseT and 10BaseF

## Slide 56: Classic Ethernet Frame Formats
Frame formats. (a) Ethernet (DIX). (b) IEEE 802.3.
  Frame format is still used with modern Ethernet.

## Slide 57: Classic Ethernet MAC Sublayer Protocol
Collision detection can take as long as 2 .
MAC protocol is 1-persistent CSMA/CD (earlier)
  Random delay (backoff) after collision is computed with BEB (Binary Exponential Backoff)
  Collisions can occur and take as long as 2 to detect
   is the time it takes to propagate over the Ethernet
  Leads to minimum packet size for reliable detection

## Slide 58: Classic Ethernet – CSMA/CD with BEB

## Slide 59: Classic Ethernet – Addressing
Each station on an Ethernet network (such as a PC, workstation, or printer) has its own network interface card (NIC).
The NIC fits inside the station and provides the station with a link-layer address.
The Ethernet address is 6 bytes (48 bits), normally written in hexadecimal notation, with a colon between the bytes. For example, the following shows an Ethernet MAC address:
4A:30:10:21:10:1A
You can use “ipconfig /all” to check the MAC addresses of your PC or laptop.

## Slide 60: Classic Ethernet – unicast and multicast address
To find the type of the address, we need to look at the second hexadecimal digit from the left.
  If it is even, the address is unicast.
  If it is odd, the address is multicast.
  If all digits are Fs, the address is broadcast.

## Slide 61: Example
Define the type of the following destination addresses:
4A:30:10:21:10:1A
47:20:1B:2E:08:EE
FF:FF:FF:FF:FF:FF
Solution
  a. This is a unicast address because A in binary is 1010 (even).
  b. This is a multicast address because 7 in binary is 0111 (odd).
  c. This is a broadcast address because all digits are Fs in
  hexadecimal.

## Slide 62: Ethernet Performance
Efficiency of Ethernet at 10 Mbps with 512-bit slot times
Efficient for large frames, even with many senders
  Degrades for small frames (and long LANs)
10 Mbps Ethernet,
64 byte min. frame

## Slide 63: Classic Ethernet – Bandwidth sharing

## Slide 64: Collision domains
A bridge is the separation of the collision domain

## Slide 65: Full-duplex Switched Ethernet

## Slide 66: Switched Ethernet (1 of 2)
(a) Hub. (b) Switch.
  Hubs wire all lines into a single CSMA/CD domain
  Switches isolate each port to a separate domain
    Much greater throughput for multiple ports
    No need for CSMA/CD with full-duplex lines

## Slide 67: Switched Ethernet (2 of 2)
An Ethernet switch
Switches can be wired to computers, hubs and switches
  Hubs concentrate traffic from computers
  More on how to switch frames the in 4.8

## Slide 68: Fast Ethernet
The original fast Ethernet cabling
Fast Ethernet extended Ethernet from 10 to 100 Mbps
  The MAC sublayer was left unchanged.
  To keep the minimum size of the frame, the maximum length of the network should be 10 times shorter
  Twisted pair (with Cat 5) dominated the market

## Slide 69: Encoding for fast Ethernet

## Slide 70: Gigabit Ethernet
(a) A two-station Ethernet. (b) A multistation Ethernet.
Switched Gigabit Ethernet is now the garden variety
  With full-duplex lines between computers/switches

## Slide 71: Gigabit Ethernet – operation mode
The address length, the frame format, and the maximum and minimum frame length are kept the same.
To achieve a data rate of 1 Gbps, this was no longer possible to keep the MAC sublayer untouched.
Gigabit Ethernet has two distinctive approaches for medium access:
  half-duplex: used with a hub. CSMA/CD required. The maximum distance is 100 times less than that in classic Ethernet (2500m25m).
  full-duplex: “normal” mode. Used in central switch. buffered. No contention, no CSMA/CD

## Slide 72: Gigabit Ethernet – network radius
Two features to the standard to increase the radius:
Carrier extension: tells the hardware to add its own padding after the normal frame(64 bytes) to extend the frame to 512 bytes.
Frame bursting: allows a sender to transmit a concatenated sequence of multiple frames in a single transmission.
These two features extend the radius of the network to 200 meters.

## Slide 73: Gigabit Ethernet -implementation
Gigabit Ethernet cabling
  Gigabit Ethernet is commonly run over twisted pair.

## Slide 74: Encoding in Gigabit Ethernet

## Slide 75: 10-Gigabit Ethernet
10-Gigabit Ethernet cabling
SR表示短距离,
LR表示长距离,
ER 表示超长距离

## Slide 76: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 77: Wireless LANs
802.11 architecture and protocol stack
802.11 physical layer
802.11 MAC sublayer protocol
802.11 frame structure
Services

## Slide 78: The 802.11 Architecture and Protocol Stack (1 of 2)
802.11 architecture. (a) Infrastructure mode. (b) Ad-hoc mode.

## Slide 79: The 802.11 Architecture and Protocol Stack (2 of 2)
Part of the 802.11 protocol stack

## Slide 80: Basic Service Set & Extended Service Set

## Slide 81: 802.11 physical layer
  NICs are compatible with multiple physical layers
    E.g., 802.11 a/b/g
Name | Technique | Max. Bit Rate
802.11b | Spread spectrum, 2.4 GHz | 11 Mbps
802.11g | OFDM, 2.4 GHz | 54 Mbps
802.11a | OFDM, 5 GHz | 54 Mbps
802.11n | OFDM with MIMO, 2.4/5 GHz | 600 Mbps

## Slide 82: Flow Diagram for CSMA/CA
CSMA/CD
节点侦听到信道空闲时立即发送；
CSMA/CA
节点推迟发送，每新尝试一次都要随机回退。避免有多个站同时等待信道空闲，并发现信道空闲后立即发送而造成的冲突。

## Slide 83: The 802.11 MAC Sublayer Protocol (1 of 4)
Sending a frame with CSMA/CA
  CSMA/CA inserts backoff slots to avoid collisions
  MAC uses ACKs/retransmissions for wireless errors

## Slide 84: The 802.11 MAC Sublayer Protocol (2 of 4)
(a) The hidden terminal problem. (b) The exposed terminal problem.

## Slide 85: The 802.11 MAC Sublayer Protocol (3 of 4)
Virtual channel sensing using CSMA/CA
Virtual channel sensing with the NAV and optional RTS/CTS (often not used) avoids hidden terminals

## Slide 86: The 802.11 MAC Sublayer Protocol (4 of 4)
Interframe spacing in 802.11
  Different backoff slot times add quality of service
    Short intervals give preferred access, e.g., control, VoIP
  MAC has other mechanisms too, e.g., power save

## Slide 87: 帧间间隔IFS (interframe space)
为了尽量避免碰撞，802.11规定，所有的站在完成发送后，必须再等待一段很短的时间（继续监听）才能发送下一帧。这段时间的通称是帧间间隔IFS。帧间间隔的长短取决于该站要发送的帧的类型。高优先级的帧需要等待的时间较短，因此可以优先获得发送权，但低优先级帧就必须等待较长的时间。
  SIFS：短帧间间隔，用来间隔需要立即响应的帧，如控制帧(RTS/CTS/ACK)等
  AIFS：任意帧间间隔。根据访问类别(即要传输的数据类型)对站点进行优先级排序，AISF的计算公式为：AISF编号*时隙+ SISF；
  DIFS：分布协调功能帧间间隔，只能够由工作于DCF模式的站点来使用
  PIFS：集中协调功能帧间间隔，只能够由工作于PCF模式的站点来使用
  EIFS: 在前一帧出错的情况下，发送节点 不得不延迟 EIFS 而不是DIFS时间段，再发送下一帧。

## Slide 88: The 802.11 Frame Structure
Format of the 802.11 data frame
  Frames vary depending on their type (Frame control)
  Data frames have 3 addresses to pass via APs

## Slide 89: Subfields in Frame Control field

## Slide 90: Addressing Mechanism

## Slide 91: Services
Association and data delivery
Security and privacy
Prioritization and power control

## Slide 92: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 93: Bluetooth
Bluetooth architecture
Bluetooth applications
Bluetooth protocol stack
Bluetooth radio layer
Bluetooth link layers
Bluetooth frame structure
Bluetooth 5

## Slide 94: Bluetooth Architecture
Two piconets can be connected to form a scatternet
Piconet master is connected to slave wireless devices
  Slaves may be asleep (parked) to save power
  Two piconets can be bridged into a scatternet

## Slide 95: The Bluetooth Protocol Stack
The Bluetooth protocol architecture
Profiles give the set of protocols for a given application
  25 profiles, including headset, intercom, streaming audio, remote control, personal area network, …

## Slide 96: Bluetooth Radio / Link Layers
Radio layer
  Uses adaptive frequency hopping in 2.4 GHz band
Link layer
  TDM with timeslots for master and slaves
  Synchronous CO for periodic slots in each direction
  Asynchronous CL for packet-switched data
  Links undergo pairing (user confirms passkey/PIN) to authorize them before use

## Slide 97: The Bluetooth Frame Structure
Typical Bluetooth data frame at (a) basic and (b) enhanced data rates.
Time is slotted; enhanced data rates send faster but for the same time; addresses are only 3 bits for 8 devices

## Slide 98: Bluetooth 5
Support for Internet of Things devices
Speed increased from 1 Mbps to 2 Mbps
Message size has gone up from 31 bytes to 255 bytes
Range indoors has gone up from 10 m to 40 m
Power requirements have been reduced slightly
Range of the beacons has gone up slightly
Slightly better security

## Slide 99: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 100: DOCSIS
Overview
  MAC sublayer performs channel allocation, configuration of quality of service, unique forwarding model
  Uses a standard MAC frame format
Ranging
  Cable modem transmits a ranging request
  CMTS (headend) determines the network delay to the cable modem and performs necessary power adjustment
Channel bandwidth allocation
  Service flows
  Request-grant process and low-latency DOCSIS

## Slide 101: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 102: Data Link Layer Switching
Uses of bridges
Learning bridges
Spanning tree bridges
Repeaters, hubs, bridges, switches, routers, and gateways
Virtual LANs
  The IEEE 802.1Q standard

## Slide 103: Learning Bridges (1 of 3)
(a) Bridge connecting two multidrop LANs. (b) Bridges (and a hub) connecting seven point-to-point stations.
A bridge operates as a switched LAN (not a hub)
  Computers, bridges, and hubs connect to its ports

## Slide 104: Learning Bridges (2 of 3)
Backward learning algorithm picks the output port:
  Associates source address on frame with input port
  Frame with destination address sent to learned port
  Unlearned destinations are sent to all other ports
Needs no configuration
  Forget unused addresses to allow changes
  Bandwidth efficient for two-way traffic

## Slide 105: Learning Bridges (3 of 3)
Protocol processing at a bridge
Bridges extend the Link layer:
  Use but don’t remove Ethernet header/addresses
  Do not inspect Network header

## Slide 106: Spanning-Tree Bridges (1 of 4)
Bridges with two parallel links
Bridge topologies with loops and only backward learning will cause frames to circulate for ever
  Need spanning tree support to solve problem

## Slide 107: Spanning-Tree Bridges (2 of 4)
A spanning tree connecting five bridges. The dashed lines are links that are not part of the spanning tree.
After the algorithm runs:
    B1 is the root, two dashed links are turned off
    B4 uses link to B2 (lower than B3 also at distance 1)
    B5 uses B3 (distance 1 versus B4 at distance 2)

## Slide 108: Spanning-Tree Bridges (3 of 4)
I think that I shall never see
A graph more lovely than a tree.
A tree whose crucial property Is loop-free connectivity.
A tree which must be sure to span.
So packets can reach every LAN.

## Slide 109: Spanning-Tree Bridges (4 of 4)
First the Root must be selected
By ID it is elected.
Least-cost paths from Root are traced
In the tree these paths are placed.
A mesh is made by folks like me
Then bridges find a spanning tree.
-- Radia Perlman
  Subset of forwarding ports for data is use to avoid loops
  Selected with the spanning tree distributed algorithm by Perlman

## Slide 110: Repeaters, Hubs, Bridges, Switches, Routers, and Gateways
(a) Which device is in which layer. (b) Frames, packets, and headers.
Devices are named according to the layer they process
  A bridge or LAN switch operates in the Link layer

## Slide 111: Virtual LANs (1 of 2)
A building with centralized wiring using hubs and a switch

## Slide 112: Virtual LANs (2 of 2)
Two VLANs, gray and white, on a bridged LAN
VLANs (Virtual LANs) splits one physical LAN into multiple logical LANs to ease management tasks
  Ports are “colored” according to their VLAN

## Slide 113: The IEEE 802.1Q Standard (1 of 2)
Bridged LAN that is only partly VLAN aware. The shaded symbols are VLAN aware. The empty ones are not.
Bridges need to be aware of VLANs to support them
  In 802.1Q, frames are tagged with their “color”
  Legacy switches with no tags are supported

## Slide 114: The IEEE 802.1Q Standard (2 of 2)
The 802.3 (legacy) and 802.1Q Ethernet frame formats
802.1Q frames carry a color tag (VLAN identifier)
  Length/Type value is 0x8100 for VLAN protocol

## Slide 115: The Medium Access Control Sublayer Chapter 4
The Channel Allocation Problem
Multiple Access Protocols
Ethernet
Wireless LANs
Bluetooth
DOCSIS
Data Link Layer Switching
Summary

## Slide 116: Summary (1 of 4)
Some networks have a single channel that is used for all communication. In these networks, the key design issue is the allocation of this channel among the competing stations wishing to use it.
FDM and TDM are simple, efficient allocation schemes when the number of stations is small and fixed and the traffic is continuous.
Both are widely used under these circumstances, for example, for dividing up the bandwidth on telephone trunks.
However, when the number of stations is large and variable or the traffic is fairly bursty—the common case in computer networks—FDM and TDM are poor choices. Numerous dynamic channel allocation algorithms have been devised.

## Slide 117: Summary (2 of 4)
The ALOHA protocol, with and without slotting, is used in many derivatives in real systems, for example, in DOCSIS networks.
As an improvement when the state of the channel can be sensed, stations can avoid starting a transmission while another station is transmitting. This technique, carrier sensing, has led to a variety of CSMA protocols for LANs and MANs. It is the basis for classic Ethernet and 802.11 networks.
A class of protocols that eliminates contention altogether, or at least reduces it considerably, has been well known for years.
  The bitmap protocol, topologies such as rings, and the binary countdown protocol completely eliminate contention.
  The tree-walk protocol reduces it by dynamically dividing the stations into two disjoint groups of different sizes and allowing contention only within one group; ideally that group is chosen so that only one station is ready to send when it is permitted to do so.
Modern versions of MAC protocols, including DOCSIS and Bluetooth, explicitly take steps to avoid contention by assigning transmission intervals to senders.

## Slide 118: Summary (3 of 4)
Wireless LANs have the added problems that it is difficult to sense colliding transmissions, and that the coverage regions of stations may differ.
In the dominant wireless LAN, IEEE 802.11, stations use CSMA/CA to mitigate the first problem by leaving small gaps to avoid collisions.
  The stations can also use the RTS/CTS protocol to combat hidden terminals that arise because of the second problem, although the overhead of RTS/CTS is so high in practice due to the exposed terminal problem that it is often not used, especially in dense environments. In contrast, many clients now use mechanisms to perform channel selection to avoid contention.
IEEE 802.11 is commonly used to connect laptops and other devices to wireless access points, but it can also be used between devices. Any of several physical layers can be used, including multichannel FDM with and without multiple antennas, and spread spectrum.
Modern versions of 802.11 include security features at the link layer, including support for authentication, as well as advanced encoding to support MIMO transmission.

## Slide 119: Summary (4 of 4)
Ethernet is the dominant form of wired LAN.
Classic Ethernet used CSMA/CD for channel allocation on a yellow cable the size of a garden hose that snaked from machine to machine. The architecture has changed as speeds have risen from 10 Mbps to 10 Gbps and continue to climb. Now point-to-point links such as twisted pair are attached to hubs and switches. With modern switches and full-duplex links, there is no contention on the links and the switch can forward frames between different ports in parallel.
With buildings full of LANs, a way is needed to interconnect them all. Plugand-play bridges are used for this purpose. The bridges are built with a backward learning algorithm and a spanning tree algorithm. Since this functionality is built into modern switches, the terms ‘‘bridge’’ and ‘‘switch’’ are used interchangeably. To help with the management of bridged LANs, VLANs let the physical topology be divided into different logical topologies. The VLAN standard, IEEE 802.1Q, introduces a new format for Ethernet frames.

## Slide 120: Copyright
This work is protected by United States copyright laws and is provided solely for the use of instructors in teaching their courses and assessing student learning. Dissemination or sale of any part of this work (including on the World Wide Web) will destroy the integrity of the work and is not permitted. The work and materials from it should never be made available to students except by instructors using the accompanying text in their classes. All recipients of this work are expected to abide by these restrictions and to honor the intended pedagogical purposes and the needs of other instructors who rely on these materials.